## Slide 1: Comparison of Energy Cost and Carbon Emissions for Air-Source Heat Pump and Natural Gas Furnaces in the US
Nathan Oliver

## Slide 2: Self-Introduction
  Education
  BS - Mechanical Engineering - New Mexico State University
  MS - Sustainable Energy Technology - Xi’an Jiaotong-Liverpool University
  Experience
  1 yr – Mechanical Engineer
  5 yrs – English / Physics Teacher
  1 yr – Project Manager
  I have lived in China for the past 8 years, and I recently moved to Denver
  Hobbies
  Skiing
  Soccer
  Hiking

## Slide 3: Introduction
  Desire to complete a building energy simulation project in 2022
  Comparison of Air-Source Heat Pumps (ASHP) and Natural Gas Furnaces in a typical US single-family home
  Energy Costs
  Carbon Emissions
  Initial project using BEOpt to compare ASHPs and natural gas furnaces in various US cities showed promising results
  Final project compared the two heating systems in all US counties

## Slide 4: Overview
  Project Flowchart
  IDF Files
  EPW Weather Files
  Python Simulation Flowchart
  Energy Costs
    Electricity
    Natural Gas
  Carbon Emissions
    Electricity
    Natural Gas
  Calculations
  Results
  Conclusions
  Future Improvements

## Slide 5: Project Flowchart – Part 1

## Slide 6: Project Flowchart – Part 1

## Slide 7: Project Flowchart – Part 1

## Slide 8: Project Flowchart – Part 1

## Slide 9: Project Flowchart – Part 1

## Slide 10: Project Flowchart – Part 2

## Slide 11: Project Flowchart – Part 2

## Slide 12: Project Flowchart – Part 2

## Slide 13
IDF Files
EPW Files
Python Simulation Flowchart

## Slide 14: IDF Files
  Created building envelope in BEOpt
  Exported two different IDF files, each with its own heating and cooling systems
  Scenario 1
    Air-Source Heat Pump
      SEER 22, 10 HSPF, Variable Speed
  Scenario 2
    Natural Gas Furnace
      95% AFUE
    AC Unit
      SEER 22
  Building envelope remained the same for every simulation, regardless of ASHRAE zone
3D Building Model in BEOpt

## Slide 15: EPW Weather Files
  Weather files for 3,128 US counties are available from NREL.
  The US contains 3,143 counties and county equivalents
  The counties with missing weather files were replaced using weather files from neighboring counties
  The NREL EPW weather file set only used 881 weather stations
  Multiple counties would use weather data from the same weather station
  Reduced simulation time by about 70%
  Washington County and neighboring counties use the same weather data from Akron Washington County Airport
Map of Colorado

## Slide 16: Python Simulation Flowchart

## Slide 17: Python Simulation Flowchart

## Slide 18: Python Simulation Flowchart

## Slide 19: Python Simulation Flowchart

## Slide 20: Python Simulation Flowchart

## Slide 21: Python Simulation Flowchart

## Slide 22: Python Simulation Flowchart

## Slide 23: Python Simulation Flowchart

## Slide 24: Python Simulation Flowchart

## Slide 25: Python Simulation Flowchart

## Slide 26: Python Simulation Flowchart

## Slide 27: Python Simulation Flowchart

## Slide 28: Energy Costs

## Slide 29: Electricity – Energy Cost
  State-level electricity and natural gas prices were used to calculate energy costs
  County-level prices were not readily available
Electricity Cost Calculation Flowchart
2020 US Residential Electricity Prices

## Slide 30: Natural Gas – Energy Cost
  Price of natural gas is listed in dollars per unit volume
  A conversion was needed to convert from volume to amount of energy
  Heat content of natural gas
  US Average - 1,037 btu/cubic foot [USEIA]
2020 US Residential Natural Gas Prices
Natural Gas Cost Calculation Flowchart

## Slide 31: Prices of Electricity and Natural Gas
  Price of Electricity to Natural Gas Ratio
  Unitless value
  US Avg – 3.0
  AK – 5.4
  FL – 1.4
  Map strongly correlates to energy cost comparison of ASHPs and natural gas furnaces
  Energy costs for ASHPs tend to be less expensive in states that are blue
Ratio of 2020 US Residential Electricity to Natural Gas Prices

## Slide 32: Carbon Emissions

## Slide 33: Natural Gas – Carbon Emissions
  Carbon emissions from burning natural gas
  52.91 kg/MMBtu [USEIA]
  Emissions from natural gas due to transportation and flaring were ignored
  Including emissions from these sources may significantly impact emissions from operating furnaces
Natural Gas Carbon Emissions Calculation Flowchart

## Slide 34: Electricity – Carbon Emissions
  Grid Subregions
  Regions defined by the North American Electric Reliability Corporation (NERC), which include different transmission organizations and balancing authorities
  Defined by the EPA to accurately determine the emission rates from different regions in the US
  Transmission Losses
  Vary depending on location
    Continental US – 5.1%
    Alaska – 5.4%
    Hawaii – 5.5%
Electricity Carbon Emissions
Calculation Flowchart

## Slide 35: Grid Subregion Carbon Emissions
US Grid Subregion Carbon Emissions Map

## Slide 36: Assigning a Grid Subregion to Each County
US Grid Subregion Map

## Slide 37: Assigning Grid Region for Each County
County Name | ZIP Code | Grid Subregion
Denver | 80010 | 
Denver | 80012 | 
Denver | 80014 | 
Denver | 80022 | 
… | … | …
Denver | 80291 | 
Denver | 80293 | 
Denver | 80294 | 
Denver | 80299 | 
ZIP Code | Grid Subregion
00010 | AKMS
00011 | AKGD
00012 | CAMX
00014 | AZNM
… | …
80010 | RMPA
… | …
99927 | AKMS
99928 | AKMS
99929 | AKMS
99950 | AKMS
List of all zip codes in every US county
(Only Denver County is shown for explanation purposes)
List of every zip code and its corresponding grid subregion

## Slide 38: Assigning Grid Region for Each County
County Name | ZIP Code | Grid Subregion
Denver | 80010 | 
Denver | 80012 | 
Denver | 80014 | 
Denver | 80022 | 
… | … | …
Denver | 80291 | 
Denver | 80293 | 
Denver | 80294 | 
Denver | 80299 | 
ZIP Code | Grid Subregion
00010 | AKMS
00011 | AKGD
00012 | CAMX
00014 | AZNM
… | …
80010 | RMPA
… | …
99927 | AKMS
99928 | AKMS
99929 | AKMS
99950 | AKMS

## Slide 39: Assigning Grid Region for Each County
ZIP Code | Grid Subregion
00010 | AKMS
00011 | AKGD
00012 | CAMX
00014 | AZNM
… | …
80010 | RMPA
… | …
99927 | AKMS
99928 | AKMS
99929 | AKMS
99950 | AKMS
County Name | ZIP Code | Grid Subregion
Denver | 80010 | 
Denver | 80012 | 
Denver | 80014 | 
Denver | 80022 | 
… | … | …
Denver | 80291 | 
Denver | 80293 | 
Denver | 80294 | 
Denver | 80299 | 

## Slide 40: Assigning Grid Region for Each County
County Name | ZIP Code | Grid Subregion
Denver | 80010 | 
Denver | 80012 | 
Denver | 80014 | 
Denver | 80022 | 
… | … | …
Denver | 80291 | 
Denver | 80293 | 
Denver | 80294 | 
Denver | 80299 | 
ZIP Code | Grid Subregion
00010 | AKMS
00011 | AKGD
00012 | CAMX
00014 | AZNM
… | …
80010 | RMPA
… | …
99927 | AKMS
99928 | AKMS
99929 | AKMS
99950 | AKMS

## Slide 41: Assigning Grid Region for Each County
  Used the value_counts() function to count the different grid regions for each county, and then find the subregion with the highest frequency
  Most counties would only have a single grid subregion
  For counties that were in two or more subregions, whichever subregion had the highest frequency would be assigned to that county
County Name | ZIP Code | Grid Subregion
Denver | 80010 | 
Denver | 80012 | 
Denver | 80014 | 
Denver | 80022 | 
… | … | …
Denver | 80291 | 
Denver | 80293 | 
Denver | 80294 | 
Denver | 80299 | 

## Slide 42: Assigning Grid Region for Each County
Python Generated
US Grid Subregion Map
USEPA
US Grid Subregion Map

## Slide 43: Electricity – Carbon Emissions
Python Generated
US Grid Subregion Map
Electricity Carbon Emissions
Calculation Flowchart

## Slide 44: Comparing ASHPs to Natural Gas Furnaces - Calculations
Annual home energy cost to operate ASHP relative to furnace/AC unit
Annual home emissions to operate ASHP relative to furnace/AC unit
  Note: AC fan energy consumption was removed. Results with fan consumption did not closely match initial BEOpt results

## Slide 45: Results

## Slide 46: Results – Energy Costs
Annual home energy cost to operate ASHP relative to furnace/AC unit by US County

## Slide 47: Results – Energy Costs
Annual home energy cost to operate ASHP relative to furnace/AC unit
by US County
Ratio of 2020 US Residential Electricity to Natural Gas Prices

## Slide 48: Results – Carbon Emissions
Annual home emissions to operate ASHP relative to furnace/AC unit by US County

## Slide 49: Results – Carbon Emissions
Annual home emissions to operate
ASHP relative to furnace/AC unit
by US County
US Grid Subregion
Carbon Emissions Map

## Slide 50: Conclusion
  ASHPs have lower emissions on the west coast and northeast US
  ASHPs tended to emit more emissions in colder environments
  Colder environments decreased ASHP COP
  Natural gas tended to be less expensive in colder regions
  Strong correlation between grid emissions and ASHP emissions relative to natural gas furnaces
  Strong correlation between electricity to natural gas price ratio and ASHP energy costs relative to natural gas furnaces
Annual home emissions to operate
ASHP relative to furnace/AC unit
by US County

## Slide 51: Future Improvements
  Adjust building envelope to conform to ASHRAE requirements for each ASHRAE zone
  Use electricity and natural gas prices on a county-level basis, instead of state-level prices
  Calculate emissions and costs based on a shorter-time interval, such as monthly, instead of annually.
  Gather results by state or by region
  Calculate annual costs, which would include upfront costs for each technology
  Improve visualizations (ex. Include Alaska and Hawaii in all maps)
ASHRAE Climate Zone Map

## Slide 52: Thank You

## Slide 53: Appendix – Electricity Prices with Table

## Slide 54: Appendix – Natural Gas Prices with Table

## Slide 55: Appendix – Elec:NG Price Ratio with Table

## Slide 56: Appendix - Equations

## Slide 57: Appendix - Equations

## Slide 58: Appendix - Equations

## Slide 59: Appendix – IDF File
  Area: 2500 sqft
  Type: 3-bed, 2 bath, 3 floors (inc. conditioned attic)
  Orientation: South
  Walls: R-45 Double Wood Stud
  Ceiling: R-60
  Slab: R-20
  Windows: Triple-pane U-Value 0.17 btu/h-ft2-R, 314 sqft
  Door: U-Value 0.20 btu/h-ft2-R, 20 sqft
  Air Leakage: ACH50
  Ducts: In finished space
  Cooling Set Point: 75 °F
  Heating Set Point: 70 °F
  Humidity Set Point: None

## Slide 60: Appendix – Correlation Heatmap

## Slide 61: Comparing ASHPs to Natural Gas Furnaces - Calculations

## Slide 62: References
Bianchi, Carlo; Fontanini, Anthony (2021, May 11): TMY3 Weather Data for ComStock and ResStock. National Renewable Energy Laboratory. 10.7799/1756695. Retrieved from https://data.nrel.gov/submissions/156
USEIA (2022, October 5). Carbon Dioxide Emissions Coefficients. USEIA. Retrieved from https://www.eia.gov/environment/emissions/co2_vol_mass.php. Natural Gas Carbon Dioxide Factor (Kg CO2/MMBtu)
USEIA (2021, December 30). Heat Content of Natural Gas Consumed. USEIA. Retrieved from https://www.eia.gov/environment/emissions/co2_vol_mass.php 2020. US Natural Gas Heat Factor (btu/ft3)
USEIA (2021, December 30). Natural Gas Prices. USEIA. Retrieved from https://www.eia.gov/dnav/ng/ng_pri_sum_a_EPG0_PRS_DMcf_a.htm. 2020 Residential Prices
USEIA (2021, November 4). State Electricity Profiles. USEIA. Retrieved from https://www.eia.gov/electricity/state/archive/2020/
USEPA (2021, September 22). eGRID Summary Tables 2019. eGRID Summary Tables (XLSX), Table 1 Tab. Retrieved from https://www.epa.gov/egrid/power-profiler#/
USEPA (2022, March 1). Power Profiler Terms, Calculations, and Data Sources. USEPA. Retrieved from https://www.epa.gov/system/files/documents/2021-09/power-profiler-terms-calculations-and-data-sources-9-21-2021.pdf
USEPA (2021, September 22). Power Profiler ZIP Code Tool with eGRID2019 Data v10.0. Power Profiler Emissions Tool 2019 (XLSX), Zip-Subregion Tab. Retrieved from https://www.epa.gov/egrid/power-profiler#/